## Slide 1
Large Language Models
& Why Decode Is the Problem
Section 2.1 — Foundations of LLM Inference
blue = compute / Prefill red = memory / Decode

## Slide 2
PART 0 — Foundations
What an LLM is, before we talk about speed

## Slide 3
P1 · What is an LLM?
An LLM does exactly ONE thing: predict the next token.
"The cat sat on the ___"
LLM
mat
62%
floor
18%
roof
9%
box
5%
...
2%
It outputs a probability for every possible next word → pick the top one → append → repeat.
Generating text = doing this tiny prediction over and over.
P1

## Slide 4
P2 · Text → Tokens → Vectors
How words become math (computers only understand numbers).
"unbelievable"
TOKENIZER
(split into pieces)
["un", "believ", "able"]
EMBEDDING
[ 0.2, -1.3, 0.9, 0.4, ... ]
each token → a vector
Meaning becomes geometry: king − man + woman ≈ queen (vectors that are close = meanings that are similar)
P2

## Slide 5
P3 · Parameters = Stored Knowledge
An LLM is a giant function with millions of tunable numbers ('weights').
SmolLM2-135M
135,000,000 parameters
Every weight must be STORED in memory
and READ for each token generated.
⚠ Seed of the whole story:
reading all these numbers, for every single token, is the bottleneck we'll meet soon.
135M params → ~141 MB at INT4 → must fit in the board's DDR3.
P3

## Slide 6
P4 · Train Once, Run Forever
TRAINING
• done ONCE · takes weeks
• needs many GPUs
• learns the weights
• then weights are FROZEN 🔒
weights
INFERENCE
• done EVERY request
• weights are fixed
• prompt in → output out
• ← OUR project lives here
Training learns the numbers. Inference uses them. We only do inference.
And inference itself splits into TWO phases →
P4

## Slide 7
P5 · The Transformer
Every modern LLM = a stack of identical decoder layers.
DECODER LAYER
DECODER LAYER
DECODER LAYER
DECODER LAYER ( × 30 )
text in
next token out
each layer =
Attention
+
Feed-Forward
(FFN)
SmolLM2-135M = 30 layers, hidden size 2048
P5

## Slide 8
PART 1 — The Story
Two phases. One bottleneck.

## Slide 9
Inference Has Two Phases
PREFILL
process the INPUT prompt
t1
t2
t3
t4
t5
• all tokens at ONCE (parallel)
• keeps hardware busy
• COMPUTE-bound
• "like training"
KV CACHE
the bridge
(grows with length)
DECODE
generate the OUTPUT
o1
o2
o3
• ONE token at a time
• sequential — can't parallelize
• MEMORY-bound
• ← the real problem
1

## Slide 10
The Autoregressive Loop
auto = self · regressive = depends on previous outputs
"The"
MODEL
"cat"
MODEL
"sat"
...
feed the output back in
One token at a time → you can't compute token #2 before token #1 exists →
no parallelism → DECODE is memory-bound.
2

## Slide 11
Inside a Decoder Layer
text
EMBEDDING
DECODER LAYER × N
LM HEAD →
next token
ATTENTION
"gather context
from other words"
latency-sensitive
(many quick comparisons)
FFN
"think about it
individually"
weight-intensive
(lots of stored data)
3

## Slide 12
Attention = Q, K, V
Q
what am I looking for?
K
what do I offer?
V
my actual content
score = Q·Kᵀ → ÷√dₖ → softmax → × V
= a context-updated vector for the word
Attention = softmax( Q·Kᵀ / √dₖ ) · V
"The bank was closed because the river flooded."
→ "bank" attends to "river" → it means LAND, not money.
4

## Slide 13
The Memory Wall — the 'aha'
performance
time
compute ↗↗↗
memory bandwidth →
THE GAP
= memory wall
Memory trade-off
Type
Speed
Density
Cost
SRAM
very fast
low
$$$
DRAM
slower
high
$
HBM
high BW
high
$$$
Decode lives in the memory-bound regime → it starves waiting for data.
No GPU/TPU was designed just for decode.
5

## Slide 14
Why a Tiny Model?
Many capable LLMs (7B, 13B, ...) — too big for the board
constraint 1: 1 GB DDR3 on ZC702
constraint 2: 64-bit AXI bus @ 93.75 MHz
constraint 3: decoder-only + GQA runtime only
SmolLM2-135M
141 MB @ INT4 · 30 layers · hidden 2048
✓ fits ✓ all kernels verified ✓ compressible
Qwen2.5-0.5B = upgrade path
(blocked: missing bias tensors → future work)
6

## Slide 15
The one sentence that ties it all together
LLM = next-token predictor
Decode is sequential
→ memory-bound
→ hits the memory wall
→ need custom hardware + a tiny model
→ this is exactly why our project exists (and what Section 2.2 builds).